EPOS- SYSTEM OBSERWACJI PŁYTY EUROPEJSKIEJ, POIR.04.02.00-14-A0003/16
Priorytet IV: ZWIĘKSZENIE POTENCJAŁU NAUKOWO-BADAWCZEGO Działanie 4.2: ROZWÓJ NOWOCZESNEJ INFRASTRUKTURY BADAWCZEJ SEKTORA NAUKI
Wartość projektu: 62 558 323,87 PLN; Dofinansowanie ze środków Europejskiego Funduszu Rozwoju Regionalnego: 47 399 281,47 PLN
PROJEKT EPOS- SYSTEM OBSERWACJI PŁYTY EUROPEJSKIEJ JEST WSPÓŁFINANSOWANY PRZEZ UNIĘ EUROPEJSKĄ ZE ŚRODKÓW PROGRAMU OPERACYJNEGO INTELIGENTNY ROZWÓJ 2014-2020

File number: FZ-1/5058/SK/19/BH					                        Katowice, 27/05/2019

Subject: Preliminary inquiry to determine the value of the contract for the planned procurement procedure

Dear Sir/Madame,

We are asking for an preliminary offer for the delivery of seismological equipment for continuous real-time monitoring of seismic events consist 5 Data Recorders + 5 tri-axial rotational  seismometers + 5 tri-axial accelerometer sensors.

The offer should include:

- Net / gross price in PLN or in other currency (price should include the cost of packet, delivery and insurance  from Seller to Buyer). The Buyer allows an offer in a other currency than PLN; for the purpose of comparison of offers, the Buyer will calculate the submitted offers in other currency than PLN in accordance with the average of NBP (National Polish Bank) exchange rate on the last day of submitting offer,

- Date and terms of delivery,

- Terms of payment,

- Terms of guarantee.

The preliminary offer should be submitted on the offer form - Annex No. 1

Requirements and technical parameters:

The subject of the contract is to provide seismological equipment for continuous real-time monitoring of seismic events in the Upper Silesian Coal Basin in Poland. Seismic network will be installed in the area of about 2000 square kilometers. The data center will be located in the building of Central Mining Institute (GIG) in Katowice. The subject of the order is five sets consisting of a digital recorder, a 	rotational seismometer and an accelerometer sensor.

We expect the following configuration:

Network for digital real time continuous seismic monitoring (5 Data Recorders + 5 tri-axial rotational  seismometers + 5 tri-axial accelerometer sensors)

Recorders:

- number of channels: 9

- ADC: 31bit

- sampling rate: up to 1000 Hz

- dynamic range: at least 130dB

- data format : miniSEED

- ethernet protocols: Seedlink, SSH, FTP, HTTP

- recording: continuous or  STA/LTA trigger

- LAN service, Wi-Fi

- remote service via the Internet

- AC 230V power supply + internal battery

- GPS receiver

- internal memory: SD card

- power for sensors: 12V

- suitcase

Rotational  seismometers:

- number of channels: 3

- resolution: rozdzielczość: 6*10-8rad/s at 1Hz

- dynamic range: at least 115dB

- frequency range: 0.05-50Hz

- temperature range: : -10 - +30oC

- weight: max. 2kg

- power suply: 10-18V

- length of the connection cable: 5m

Accelerometer sensors:

- number of channels: 3

- full scale: ±3g

- dynamic range: at least 130dB

- frequency range: up to 120Hz

- temperature range: : -30 - +50oC

- weight: max. 1kg

- power suply: 10-16V

- length of the connection cable: 5m

Place and date for submission of offers

The offer must be submitted by  the  04/06/2019. The offer can be submitted electronically or at the Buyer:

Główny Instytut Górnictwa (Central Mining Institute)

Commercial Department  (FZ-1)

Plac Gwarków 1

40-166 Katowice

Poland

e-mail address: skolinska@gig.eu

Commercial contact:

Monika Wallenburg 		- tel. 0048 32 259 25 47,  e-mail: mwallenburg@gig.eu

Sylwia Kolińska       		- tel. 0048 32 259 25 55,  e-mail: skolinska@gig.eu

WE INVITE YOU TO SUBMIT OFFERS

Sincerely,
  Head of Commercial Department

M.A.  Monika Wallenburg

Annex No. 1

EPOS- SYSTEM OBSERWACJI PŁYTY EUROPEJSKIEJ, POIR.04.02.00-14-A0003/16
Priorytet IV: ZWIĘKSZENIE POTENCJAŁU NAUKOWO-BADAWCZEGO Działanie 4.2: ROZWÓJ NOWOCZESNEJ INFRASTRUKTURY BADAWCZEJ SEKTORA NAUKI
Wartość projektu: 62 558 323,87 PLN; Dofinansowanie ze środków Europejskiego Funduszu Rozwoju Regionalnego: 47 399 281,47 PLN
PROJEKT EPOS- SYSTEM OBSERWACJI PŁYTY EUROPEJSKIEJ JEST WSPÓŁFINANSOWANY PRZEZ UNIĘ EUROPEJSKĄ ZE ŚRODKÓW PROGRAMU OPERACYJNEGO INTELIGENTNY ROZWÓJ 2014-2020

File number: FZ-1/5058/SK/19/BH

Preliminary offer for the delivery of seismological equipment for continuous real-time monitoring of seismic events consist 5 Data Recorders + 5 tri-axial rotational  seismometers + 5 tri-axial accelerometer sensors

Name/ Name and surname of Seller:

……………………………………………..

Address: …………………………………..

Telephone number: ……………………….

E-mail address: …………………………….

Contact person: …………………………….

| No. | Specification | Unit of measure | Quantity | Net unit price ……..* | Net total value ………* | VAT tax amount …….* | Gross total value …….* |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 |
| 1 |  |  |  |  |  |  |  |
| 2 |  |  |  |  |  |  |  |
| 3 |  |  |  |  |  |  |  |
| TOTAL: |  |  |  |

* Currency to be indicated

In the case of foreign Seller  who have not a branch in Poland only the blank spaces from 1 to 6  (net unit price and net total value) should be filled in.

In the case of a Polish Seller  or Foreign Seller  possessing a branch on the  territory of Poland all blank spaces should be filled in independently on the given currency.

- Date and terms of delivery: ……………………………………

- Terms of payment: ……………………………………………..

- Terms of guarantee: ………………………………..…………..

Information clause from Article 13 GDPR (General Data Protection Regulation):

According to Article 13, paragraph 1 and 2 of Regulation (EU) 2016/679 of the European Parliament and Council of 27 April, 2016 on the protection of natural person with regard to the processing of personal data and on the free movement of such data and repealing Directive 95/46 / EU (general regulation on data protection) (Journal of Laws EU L 119 of 04.05.2016, page 1), hereinafter "GDPR", we informs that:

- the administrator of your personal data is:

Główny Instytut Górnictwa (Central Mining Institute)

Plac Gwarków 1

40 - 166 Katowice

Poland

- the inspector of personal data protection at the Główny Instytut Górnictwa (Central Mining Institute) is Mrs.

M. Sc Katarzyna Kareł, e-mail: gdpr@gig.eu

- Your personal data will be processed on the basis of Article 6, paragraph 1, letter c GDPR for the purpose of this inquiry;

- the recipients of the Seller’s personal data will be persons or entities to whom the documentation regarding this preliminary inquiry will be made available,
- the Seller's personal data will be kept for 4 years,

- in relation to Your personal data, decisions will not be taken in an automated manner, application to Article 22 GDPR;

- You have the right:

- based on Article 15 GDPR the right of access to Your personal data relating to;

- based on Article 16 GDPR right to rectify Your personal data;

- based on Article 18 GDPR the right to request the administrator to restrict the processing of personal data, subject to the cases referred to in Article 18, paragraph 2 GDPR;

- the right to file a complaint to the President of the Office for Personal Data Protection, if you decide that the processing of your personal data concerning you violates the provisions of the GDPR;

- You are not entitled to:

- according to Article 17, paragraph 3, letter b,  d  or  e  GDPR right to delete personal data;

- the right to transfer personal data referred to Article 20 GDPR;

- based on Article 21 GDPR right to object to the processing of personal data, as the legal basis for the processing of Your personal data is Article 6, paragraph 1, point c GDPR.

.............................................................					.............................................................

Place, date						                      Signature